## Slide 1
By Gouasmia Zakaria– may 24, 2019
Intelligent mobile Robotics
& Perception Systems
Notes: Today we gonna see the intelligent mobile robotic and perception System .

## Slide 2
Presentation Overview
01
Introduction
02
Robot Hardware
03
Environment Representation
04
AI/ML Applied on Robotics Perception
Case studies
&
Conclusions
Notes: In the overview of this PPT . We will start with simple introduction and definition to Robot hardware (for move and perception) then the Environment representation then ……

## Slide 3
Robots and Artificial Intelligence
Notes: The definition of robotics may not be very clear till today, but they are indeed our future. Not everyone is so interested in the prospect of a radical change that robots are about to bring, but we are embracing the technology and working out how to best collaborate with it. Robots are not new – in fact, we’ve been seeing them since the ever popular Terminator movies as evil assassin robots.
Artificial Intelligence (AI), on the other hand, is the next generation of robotics that involves intelligent machines that work and react like humans. It is often called as machine intelligence and has been around for quite some time now.

## Slide 4
What is Robots ?
Notes: Robots are programmable machines specifically programmed to carry out a complex series of tasks without any human intervention.
robots are becoming more capable and more diverse than ever. Robots are often characterized by their capabilities in performing dull to dangerous tasks, easily and without needing humans to perform them.

## Slide 5
Difference between Robots and Artificial Intelligence
Notes: Most people would think robots and artificial intelligence (AI) are one and the same, but they are very different terms associated with different fields.
Robots are hardware and AI is software.
In technical terms, robots are machines designed to execute one or more simple to complex tasks automatically with utmost speed and precision, whereas AI is like a computer program that typically demonstrates some of the behaviors associated with human intelligence like learning, planning, reasoning, knowledge sharing, problem solving, and more.

## Slide 6
Artificial Intelligence and Machine Learning in the Industrial Robotics Application
Notes: Artificial Intelligence and Machine Learning in the Industrial Robotics Application
Artificial intelligence (AI) and machine learning capabilities have been quickly making their way into industrial robotics technology.
In the never-ending quest to improve productivity, manufacturers are looking to improve the inflexible capabilities of standard industrial robots.
The merging of robotics and AI technology has several consequences, and early adopters of these new robotic systems are reaping the benefits. The technology, while relatively new, is widely available and impacts manufacturing processes in a number of ways.

## Slide 7
Types of Robots :
Manipulators
  based of the workplace.
  (Common industrial robots)
2. Mobile Robots
  Move using wheels, legs, etc.
  Examples: delivering food in hospitals,
  autonomous navigation, surveillance, etc.
Notes: And for robots types we have 3 types :

## Slide 8
Types of Robots :
3.Hybrid (mobile with manipulators)
    Examples: humanoid robot
    (physical design mimics human torso)
    Made by Honda Corp. in Japan.
Notes: For the hybrid robots it’s contain both manipulators and mobile robots

## Slide 9
Robot Hardware
Notes: Now going to the robot hardware what exactly the things making the robot act and see like human

## Slide 10
Robots are equipped with effectors & Actuators.
Effectors Actuators
Assert a force on Communicates a
the environment command to an effector
Notes: 1- As the man have receptors the robot are equipped with effectors & Actuators.
*
*
*
and all of that called sensors

## Slide 11
Effectors
• an effector is any device that affects the environment.
• a robot’s effector is controlled by the robot.
• effectors can range from legs and wheels to arms and fingers
• controller has to get effectors to produce desired effect on the environment, based on robot’s task
Notes: now more about effectors

## Slide 12
Actuators
•an actuator is the actual mechanism that enables the effector to execute an action
• typically include:
– electric motors
– hydraulic cylinders
– pneumatic cylinders
Notes: 1- And an actuator is the actual mechanism that enables the effector to execute an action

## Slide 13
Sensors
Examples of sensors:
Tactile sensors (whiskers, bump panels)
Global Positioning System (GPS)
Imaging sensors (camera )
Notes: 1-So the sensors is a device that detects and responds to some type of input from the physical environment.
2- Examples of sensors:

## Slide 14
Sensors:
Passive sensors.
    True observers such as cameras.
b. Active sensors
    Send energy into the environment,
    like sonars.
Notes: We already explain what is sensors .because nowadays
The robot are equipped with sensors
Passive sensors
Active sensors

## Slide 15
Notes: This is an example of true Passive sensors

## Slide 16
Notes:     And This is an example of Active sensors who Send energy into the environment, like sonars.

## Slide 17
Alternative vehicle designs
‘Car’- steer and drive
Two drive wheels and castor
2DoF – Non-H
Three wheels that both steer and drive
Notes: And for each mobile robot who have sensor and some of them also have some physical mechanism to make it able to move .
Those are the most used vehicle designs in robotic

## Slide 18
Degrees of freedom
General meaning: How many parameters needed to specify something?
E.g. for an object in space have:
  X,Y,Z position
  Roll, pitch, yaw rotation
  Total of 6 degrees of freedom
So .How many d.o.f. to specify a vehicle on a flat plane?
Notes: If we talked about move we must know the degrees of freedom about this kind of movement .
And As a general meaning it is How many parameters needed to specify something?

## Slide 19
Notes: Degree of freedom counts one for each independent direction
of movement.
6 degrees of freedom are required to place
an object at a particular orientation.

## Slide 20
Degrees of freedom
In relation to robots could consider:
How many joints/articulations/moving parts?
How many individually controlled moving parts?
How many independent movements with respect to a co-ordinate frame?
How many parameters to describe the position of the whole robot or its end effector?
Notes: Degree of freedom is

## Slide 21
Degrees of freedom
How many moving parts?
  If parts are linked need fewer parameters to specify them.
How many individually controlled moving parts?
  Need that many parameters to specify robot’s configuration.
  Often described as ‘controllable degrees of freedom’
  But note may be redundant e.g. two movements may be in the same axis
  Alternatively called ‘degrees of mobility’

## Slide 22
Notes: Those some real example for mobile robots
This for ‘Car’- steer and drive

## Slide 23
Notes: And this contain many wheels each one can drive

## Slide 24
Notes: This is very famous kind of wheels for robots today

## Slide 25
Robot locomotion
01
02
03
07
06
05
Walking
Swimming
Hopping
Rolling
Slithering
Running
Robot locomotion is the collective name for the various methods that robots use to transport themselves from place to place.
Types of locomotion
04
Hybrid
06
Metachronal motion
Notes: 1-And now to the important chapter of the robot locomotion
2-Robot locomotion is the collective name for the various methods that robots use to transport themselves from place to place.
-tires robots are typically quite energy efficient and simple to control. However, other forms of locomotion may be more appropriate for a number of reasons, for example traversing rough terrain, as well as moving and interacting in human environments..
-A major goal in this field is in developing capabilities for robots to autonomously decide how, when, and where to move. However, coordinating a large number of robot joints for even simple matters, like negotiating stairs, is difficult.
Types of locomotion
1.1 Walking
1.2 Bipedal walking
1.3 Running
1.4 Rolling
1.5 Hopping
1.6 Metachronal motion
1.7 Slithering
1.8 Swimming
1.9 Brachiating
1.10 Hybrid

## Slide 26
01
Walking
A leg mechanism is an assembly of links and joints intended to simulate the walking motion of humans or animals.
Mechanical legs can have one or more actuators, and can perform simple planar or complex motion.
Compared to a wheel, a leg mechanism is potentially better fitted to uneven terrain, as it can step over obstacles.
Robot locomotion
Notes: Just as example of walking robot

## Slide 27
Robot locomotion
02
Swimming
An autonomous underwater vehicle (AUV) is a robot that travels underwater without requiring input from an operator.

## Slide 28
Evolution of robotic sensors
Historically, robotic sensors have become richer and richer
1960s: Shakey
1990s: Tourguide robots
2010s: Willow Garage PR2
2010s: SmartTer – the autonomous car
Reasons:
  Commodization of consumer electronics
  More computation available to process the data
Notes: 1-The evolution of robotic sensors
Historically, robotic sensors have become richer and richer
We will see those exemples
And the reasons for this advancement is the :
  Commodization of consumer electronics
  More computation available to process the data

## Slide 29
Shakey the Robot (1966-1972), SRI International
Operating environment
  Indoors
  Engineered
Sensors
  Wheel encoders
  Bumb detector
  Sonar range finder
  Camera

## Slide 30
Rhino Tourguide Robot (1995-1998), University of Bonn
Operating environment
  Indoors (Museum: unstructured and dynamic)
Sensors
  Wheel encoders
  Ring of sonar sensors
  Pan-tilt camera

## Slide 31
Willow Garage PR2 2010s
Operating environment
  Indoors and outdoors
  Onroad only
Sensors
  Wheel encoders
  Bumper
  IR sensors
  Laser range finder
  3D nodding laser range finder

## Slide 32: The SmartTer Platform (2004-2007)
ASL
Autonomous Systems Lab
Motion Estimation / Localization
Differential GPS system
(Omnistar 8300HP)
Inertial measurement unit
(Crossbow NAV420)
Optical Gyro
Odometry
(wheel speed, steering angle)
  Motion estimation
  Localization
Internal car state sensors
  Vehicle state flags (engine, door, etc.)
  Engine data, gas pedal value
Camera for life video streaming
  Transmission range up to 2 km
 Three navigation SICK laser scanners
Obstacle avoidance and local navigation
 Two rotating laser scanners (3D SICK)
3D mapping of the environment
Scene interpretation
 Omnidirectional camera
Texture information for
the 3D terrain maps
Scene interpretation
 Monocular camera
Scene interpretation
Notes: And then The SmartTer Platform are more modern then all the others with very hight revolution in camera with life video streaming and sonsors
And also the localization and estimation

## Slide 33: deep-learning based multimodal detection and tracking system
ASL
Autonomous Systems Lab
Pedestrians
Cars
Rich info
Inexpensive
Noise
No distance
High prec
Low info
Light independent
Man legs
Notes: Multimodal detection and tracking system
Using deep learning algorithm to obtain
The ability to detect people in real-world environments is crucial for a wide variety of applications including video surveillance and intelligent driver assistance systems.
The detection of pedestrians is the next logical step after the development of a successful navigation and obstacle avoidance algorithm for urban environments.
However, pedestrians are particularly difficult to detect because of their high variability in appearance due to clothing, illumination and the fact that the shape characteristics depend on the viewpoint
And Using deep learning algorithm we can detect those and giving the meaning for the picture toked by the robot sensor

## Slide 34
Detection and tracking displayed on camera data
Detection and tracking displayed on laser data
What the robot sees: laser projected on image
Notes: This is the most 3 kind of data used in Detection and tracking displayed
Camera
Prjlaser
Laser

## Slide 35
Sensors: outline
Optical encoders
Heading sensors
  Compass
  Gyroscopes
Accelerometer
IMU
GPS
Range sensors
  Sonar
  Laser
  Structured light
Vision (next lectures)
Notes: As more information about sensors outline we already said there is
Optical encoders
Heading sensors
  Compass
  Gyroscopes
Accelerometer
IMU
GPS
Range sensors
  Sonar
  Laser
  Structured light
Vision (next lectures)

## Slide 36
ASL
Autonomous Systems Lab
Wheel / Motor Encoders
Use cases
  measure position or speed of the wheels or steering
  integrate wheel movements to get an estimate of the position -> odometry
  optical encoders are proprioceptive sensors
  typical resolutions: 64 - 2048 increments per revolution.
  for high resolution: interpolation
Working principle of optical encoders
  regular: counts the number of transitions but cannot tell the direction of motion
  quadrature: uses two sensors in quadrature-phase shift. The ordering of which wave produces a rising edge first tells
the direction of motion. Additionally, resolution is 4 times bigger
  a single slot in the outer track generates a reference pulse per revolution
23

## Slide 37: Heading Sensors
ASL
Autonomous Systems Lab
Definition:
  Heading sensors are sensors that determine the robot’s orientation and inclination with
respect to a given reference
Heading sensors can be proprioceptive (gyroscope, accelerometer) or
exteroceptive (compass, inclinometer).
Allows, together with an appropriate velocity information, to integrate the movement to a position estimate.
  This procedure is called deduced reckoning (ship navigation)

## Slide 38
Encoders
Definition:
  electro-mechanical device that converts linear or angular position of a shaft to an analog or digital signal, making it an linear/anglular transducer

## Slide 39: Motion-Capture Systems
Autonomous Mobile Robots
ASL
Autonomous Systems Lab
Vicon and Optitrack
  System of several cameras that track the position of reflective markers
  >300 fps
  <1 mm precision
  Suitable for ground-truth comparison, control stragies, (e.g., quadrotors)
  Indoor or outdoor application
  Require preinstallation and precalibration of the cameras (done with a special
calibration rig moved by the user)
Notes: Vicon and Optitrack
Is System of several cameras that track the position of reflective markers
Indoor motion capture systems like VICON and Optitrack can be used to provide position and attitude data for vehicle state estimation, or to serve as ground-truth for analysis.
The motion capture data can be used to update the local position estimate relative to the local origin.
Heading (yaw) from the motion capture system can also be optionally integrated by the attitude estimator.

## Slide 40
Perception In robotics
Notes: After the locomotion the perception is also important for robotics,
-Perception is a process to interpret, acquire, select and then organize the sensory information that is captured from the real world. Also perception is understood as a system that provide the robot with the ability to perceive, comprehend, and reason about the surrounding environment.
- For example: Human beings have sensory receptors such as touch, taste, smell. So, the information received from these receptors is transmitted to human brain to organize the received information.
According to this information, action is taken by interacting with the environment to manipulate and navigate the objects.
Perception and action are very important concepts in the field of Robotics. The following slides will show more details about it .

## Slide 41
Understanding = raw data + (probabilistic) models + context
Intelligent systems interpret raw data according to probabilistic models and using contextual information that gives meaning to the data.
Perception is hard!
Notes: So . Perception technically is hard!

## Slide 42
Perception is hard!
“In robotics, the easy problems are hard and the hard problems are easy”
  S. Pinker. The Language Instinct. New York: Harper Perennial Modern Classics, 1994
beating the world’s chess master: EASY (alpha go)
create a machine with some “common sense”: very HARD
Notes: And Dr pinker said In robotics, the easy problems are hard and the hard problems are easy

## Slide 43
Autonomous Mobile Robots
Margarita Chli, Paul Furgale, Marco Hutter,
Martin Rufli, Davide Scaramuzza, Roland Siegwart
Comp
Inf
g
in
ss
re
or
n
matio
Raw Data
Vision, Laser, Sound, Smell, …
Features
Corners, Lines, Colors, Phonemes, …
Objects
Doors, Humans, Coke bottle, car , …
Places / Situations
A specific room, a meeting situation, …
Navigation
Interaction
Servicing / Reasoning
Cabinet
Table
Kitchen
Autonomous Mobile Robots
Margarita Chli, Paul Furgale, Marco Hutter,
Comp
Inf
g
in
ss
re
or
n
matio
Raw Data
Vision, Laser, Sound, Smell, …
Features
Corners, Lines, Colors, Phonemes, …
Objects
Doors, Humans, Coke bottle, car , …
Places / Situations
A specific room, a meeting situation, …
Navigation
Interaction
Servicing / Reasoning
Cabinet
Table
Kitchen
Perception for Mobile Robots
Table
Oven Drawers
Notes: This is how the process going on
Firstly we need to collect data information in the data raw using vision, smell and the other sensors
Then the navigation : the robot begin the treatment of this data to give a meaning to it . The features ( corners , lines , colours )
After that the interaction also objects recognize and then begin the servicing or reasoning to recognize the situations or places

## Slide 44
Notes: The key components of a perception system are essentially sensory data processing, data representation (environment modeling), and ML-based algorithms.
Since strong AI is still far from being achieved in real-world robotics applications, this chapter is about weak AI, i.e., standard machine learning approaches .
And for this figure
It’s The Key modules of a typical robotic perception system:
  The sensory data processing (focusing here on visual and range perception);
  data representations specific for the tasks at hand; algorithms for data analysis and interpretation (using AI/ML methods);
  and planning and execution of actions for robot-environment interaction.
  Robotic perception is conclusive for a robot to make decisions, plan, and operate in real-world environments, by means of numerous functionalities and operations from occupancy grid mapping to object detection.

## Slide 45
Machine learning and Perception
Notes: Nowadays, most of robotic perception systems use machine learning (ML) techniques, ranging from classical to deep-learning approaches

## Slide 46
Machine learning and Perception
Machine learning for robotic perception can be in the form of unsupervised learning, or supervised classifiers using handcrafted features, or
deep-learning neural networks .
Notes: 1-Machine learning for robotic perception can be in the form of unsupervised learning, or supervised classifiers using handcrafted features, or
deep-learning neural networks .
2-Regardless of the ML approach considered, data from sensor(s) are the key ingredient in robotic perception. Data can come from a single or multiple sensors, usually mounted onboard the robot, but can also come from the infrastructure or from another robot .

## Slide 47
Sensor-based environment representation/mapping
Notes: Sensor-based environment representation/mapping is a very important part of a robotic perception system.
Mapping here encompasses both the acquisition of a metric model and its semantic interpretation, and is therefore a synonym of environment/scene representation

## Slide 48
Localization
Navigation
Perception functions
Notes: Robot perception functions, like localization and navigation, are dependent on the environment where the robot operates. Essentially, a robot is designed to operate in two categories of environments: indoors or outdoors. Therefore, different assumptions can be incorporated in the mapping (representation) and perception systems considering indoor or outdoor environments.
-Localization involves one question: Where is the robot now? Or, robo-localization , where am I, keeping in mind that "here" is relative to some landmark (usually the point of origin or the destination) and that you are never lost if you don't care where you are.
-Navigation comprises everything a robot needs to get from point A to point B as efficient as possible without bumping into furniture, walls or people.

## Slide 49
Environment representation
Notes: Among the numerous approaches used in environment representation for mobile robotics, and for autonomous robotic-vehicles, the most influential approach is the occupancy grid mapping

## Slide 50
Notes: After collecting the data from environment now we need to choose model such as mapping; 2d-3d grids for the Environment representation step

## Slide 51
The occupancy Grid mapping
Notes: This 2D mapping is still used in many mobile platforms due to its efficiency, probabilistic framework, and fast implementation.
Although many approaches use 2D-based representations to model the real world, presently 2.5D and 3D representation models are becoming more common.
The main reasons for using higher dimensional representations are essentially twofold:
robots are demanded to navigate and make decisions in higher complex environments where 2D representations are insufficient;
(2) current 3D sensor technologies are affordable and reliable, and therefore 3D environment representations became attainable.

## Slide 52
Robotic mapping
Notes: Robotic mapping
Mapping is the problem of integrating the information gathered with the robot’s sensors into a given representation. It can intuitively be described by the question “What does the world look like?”
Central aspects in mapping are the representation of the environment and the interpretation of sensor data .

## Slide 53
Mapping
This semantic mapping process uses ML at various levels, e.g., reasoning on volumetric occupancy and occlusions, or identifying, describing, and matching optimally the local regions from different time-stamps/models, i.e., not only higher level interpretations. However, in the majority of applications, the primary role of environment mapping is to model data from exteroceptive sensors, mounted onboard the robot, in order to enable reasoning and inference regarding the real-world environment where the robot operates.
Notes: This semantic mapping process uses ML at various levels, e.g., reasoning on volumetric occupancy and occlusions, or identifying, describing, and matching optimally the local regions from different time-stamps/models .
not only higher level interpretations.
However, in the majority of applications, the primary role of environment mapping is to model data from exteroceptive sensors, mounted onboard the robot, in order to enable reasoning and inference regarding the real-world environment where the robot operates.

## Slide 54
Artificial intelligence and machine learning applied in robotics perception
Notes: Machine learning is the science of pattern recognition and computational learning theory in artificial intelligence.
Machine learning focuses on the construction and study of algorithms that learn from and make predictions on data. In order to ensure more robust robot perception in light of unpredictable, dynamic, and noisy real- world scenarios, scientists pair machine learning approaches with biologically-inspired sensor systems.

## Slide 55
Case studies
Notes: Now we will see some of project still on studies
Like

## Slide 56
The Strands project
Notes: The Strands project is formed by six universities and two industrial partners.
The aim object of the project is to develop the next generation of intelligent mobile robots, capable of operating alongside humans for extended periods of time.
While research into mobile robotic technology has been very active over the last few years , robotic systems that can operate robustly, for extended periods of time, in human-populated environments remain a rarity. Strands aims to fill this gap and to provide robots that are intelligent,

## Slide 57
Notes: This figure shows a high level overview of the Strands system :
the mobile robot navigates autonomously between a number of predefined waypoints.
A task scheduling mechanism dictates when the robot should visit which waypoints, depending on the tasks the robot has to accomplish on any given day.
The perception system consists, at the lowest level, of a module which builds local metric maps at the waypoints visited by the robot. These local maps are updated over time, as the robot revisits the same locations in the environment, and they are further used to segment out the dynamic objects from the static scene .

## Slide 58
The AUTOCITS project
Notes: The AUTOCITS (https://www.autocits.eu/) project will carry out a comprehensive assessment of cooperative systems and autonomous driving by deploying real-world Pilots, and will study and review regulations related to automated and autonomous driving. AUTOCITS, cofinanced by the European Union through the Connecting Europe Facility (CEF) Program, aims to facilitate the deployment of autonomous vehicles in European roads, and to use connected/cooperative intelligent transport systems (C-ITS) services to share information between autonomous vehicles and infrastructure, by means of V2V and V2I communication technology, to improve safety and to facilitate the coexistence of autonomous cars in real-world traffic conditions. The AUTOCITS Pilots, involving connected and autonomous vehicles (including autonomous shuttles, i.e., low-speed robot-vehicles), will be deployed in three major European cities in “the Atlantic Corridor of the European Network”: Lisbon (Portugal), Madrid (Spain), and Paris (France).

## Slide 59
Conclusions
Notes: So just how capable is current perception and AI, and how close did/can it get to human-level performance?
DR zeliski in his introductory book to computer vision said that traditional vision struggled to reach the performance of a 2-year old child, but today’s CNNs reach super-human classification performance on restricted domains
The recent surge and interest in deep-learning methods for perception has greatly improved performance in a variety of tasks such as object detection, recognition, semantic segmentation, etc. One of the main reasons for these advancements is that working on perception systems lends itself easily to offline experimentation on publicly available datasets, and comparison to other methods via standard benchmarks and competitions.
*** the end *****
Machine learning (ML) and deep learning (DL), the latter has been one of the most used keywords in some conferences in robotics recently, are consolidated topics embraced by the robotics community nowadays. While one can interpret the filters of CNNs as Gabor filters and assume to be analogous to functions of the visual cortex, currently, deep learning is a purely nonsymbolic approach to AI/ML, and thus not expected to produce “strong” AI/ML. However, even at the current level, its usefulness is undeniable, and perhaps, the most eloquent example comes from the world of autonomous driving which brings together the robotics and the computer vision community. A number of other robotics-related products are starting to be commercially available for increasingly complex tasks such as visual question and answering systems, video captioning and activity recognition, large-scale human detection and tracking in videos, or anomaly detection in images for factory automation.

## Slide 60
THANK YOU
Notes: So just how capable is current perception and AI, and how close did/can it get to human-level performance?
DR zeliski in his introductory book to computer vision said that traditional vision struggled to reach the performance of a 2-year old child, but today’s CNNs reach super-human classification performance on restricted domains
The recent surge and interest in deep-learning methods for perception has greatly improved performance in a variety of tasks such as object detection, recognition, semantic segmentation, etc. One of the main reasons for these advancements is that working on perception systems lends itself easily to offline experimentation on publicly available datasets, and comparison to other methods via standard benchmarks and competitions.
*** the end *****
Machine learning (ML) and deep learning (DL), the latter has been one of the most used keywords in some conferences in robotics recently, are consolidated topics embraced by the robotics community nowadays. While one can interpret the filters of CNNs as Gabor filters and assume to be analogous to functions of the visual cortex, currently, deep learning is a purely non symbolic approach to AI/ML, and thus not expected to produce “strong” AI/ML. However, even at the current level, its usefulness is undeniable, and perhaps, the most eloquent example comes from the world of autonomous driving which brings together the robotics and the computer vision community. A number of other robotics-related products are starting to be commercially available for increasingly complex tasks such as visual question and answering systems, video captioning and activity recognition, large-scale human detection and tracking in videos, or anomaly detection in images for factory automation.